## Slide 1: Open Network Automation Platform (ONAP) Use Case Driven Architecture Proposal
DRAFT

## Slide 2: Outline
Requirements from ONAP Use cases
Merger Architecture Proposal Overview
Merger Architecture Highlights

## Slide 3: Contributors:
Vimal Begwani (AT&T)
Dean Bragg (AT&T)
Lingli Deng (CMCC)
Christopher Donley (Huawei)
Rajesh Gadiyar (Intel)
Xiaojun Xie (ChinaTelecom)
Alla Goldner (Amdocs)
Ranny Haiby (Nokia)
Jason Hunt (IBM)
Roberto Kung (Orange)
Xinhui Li (VMW)
Dhananjay Pavgi (TechMahindra)
Phil Robb (LF)
David Sauvageau (Bell Canada)
Stephen Terrill (Ericsson)
Huabing Zhao (ZTE)

## Slide 4: Outline
Requirements from ONAP Use cases
Merger Architecture Proposal Overview
Merger Architecture Highlights

## Slide 5: Use Case 1: vVoLTE
SPTN /
WAN
GW
Edge DC
Core
DC
GW
OS
vMME
OS
vI/SCSCF
OS
vTAS
OS
vPCSCF
OS
vHSS
OS
vSBC
OS
vPCRF
VXLAN
VXLAN
VXLAN
Overlay
Underlay
OSPF
MPLS-TP / MPLS BGP L3VPN
OSPF
Control Plane
EBGP-EVPN
OS
vSPGW

## Slide 6: High Level Requirements:
Functional Requirements:
  Onboard VoLTE VNFs, Design and Create vVoLTE Services (topology, workflow, policy, analysis)
  Deploy Artifacts
  Fault detection, correlation and policy based auto-healing
  Performance Monitoring and policy based auto scaling
  Standard ETSI-NFV interfaces integrate with vendor provided VNFM
  Integrate with vendor provided EMS
  Integrate with third party controller
  Leverage capabilities of different infrastructure environment
Platform Requirements:
  Support for Orchestration of complex deployment
  ETSI NFV Interface With Vendor Provided VNFM / EMS
  Interface with third party controller and multiple Cloud Infrastructures
  Easy to Use Closed Loop Automation Design
Notes: Requirements:
  Onboard Various VNFs
  Deploy Artifacts
  Initial Deployment / Instantiation
  Scaling up / down automatically
  Fault detection and correlation
  Auto-healing
  Standard ETSI-NFV interfaces integrate with vendor provided VNFM
  Integrate with vendor provided EMS
  Integrate with third party controller
Challenges / Gaps:
  Orchestration for complex deployment
  Closed Loop Automation

## Slide 7: Use Case 2: vCPE

## Slide 8: High Level Requirements:
Functional Requirements:
  Onboarding, Creation and Design of Virtualized Residential Broadband Service
  Customer ordering – Instantiation, Per service activation, Cut service
  Self-service -- Tiered bandwidth, Bandwidth on Demand
  Software management – Upgrade, Delete
  Auto-healing -- Automatic reboot/restart, Rebuild
  Fault detection and correlation between L2-L3 connectivity services and Internet, VoIP, Video applications
  Manage localized broadband services by automatically performing the healthcheck of the access connectivity, virtual switching/routing and auditing of service-related configurations
  Deliver high availability service requirements for emergency communications and surveillance services
Platform Requirements:
  Easy to use Change Management Design & Execution
  Easy to Use Closed Loop Automation Design
  End2end fault/alert report, events and monitoring data collection from infrastructure to service
Notes: Request clarification on topology driven orchestration. If not clear, suggest to remove.

## Slide 9: Proposed Requirements to Support two Use Cases:
ONAP Use case Functional Requirements
Requirement 1: ONAP Controller Framework to Provide Easy to Add Adaptor(s) for vendor provided VNF Managers, when necessary (Use case 1 & 2)
Requirement 2: ONAP Controller Framework to Provide Easy to Add Adaptors for external controller (Use case 1 & 2)
Requirement 3: ONAP SDC to Implement Template Driven Closed Loop Automation (Use case 1 & 2)
Requirement 4: ONAP SDC to onboard TOSCA based VNFs (Use case 1 & 2)
Requirement 5: ONAP SDC to easily create LCM workflow for Service Template (Use case 1&2)
Requirement 6: ONAP to Provide a Framework for Designing, Scheduling and Executing Planned Changes, Including Software Upgrades (Use Case 2)
ONAP Platform Requirements:
Requirement 7: Provide Tools for Vendor Self-Service VNF Certification (VNF SDK)
Requirement 8: Simplify ONAP Platform Deployment and Management by Introducing ONAP Controller
Requirement 9: Resources & Placement Optimization
Requirement 10: Support for Multiple Infrastructure Environments
Notes: Suggest to remove requirement 1: ONAP Orchestrator to include a declarative topologically-driven approach to orchestration, in addition to imperative BPMN/BPEL capabilities(Use case 1 & 2)

## Slide 10: Outline
Requirements from ONAP Use cases
Merger Architecture Proposal Overview
Merger Architecture Highlights

## Slide 12: ONAP Merger Architecture Proposal
Mediation Layer
Design-time
Service Design
Policy Creation
Analytic Application Creation
Recipie/
Engineering Rules & Policy Distribution
SDC
VNF SDK
Dashboard OA&M
(VID)
A&AI
DCAE
SDN Agent
(SDN-O)
SDN Hub Driver
VF-C
NFV-O
SDN-C
APP-C
Service
Orchestrator
GS-O
External Data Movement & APIs
Common Service
Controllers
Microservice Bus
Multi-VIM
NFV-O NFV Collector
(Monitor)
Run-time
Portal
OPEN-O UI
(GUI/CLI)
Integration
Cloud & WAN
OpenStack
Azure
VMware
RackSpace
......
UI Server
E-Services
BSS/OSS
Big Data
Policy
From
openECOMP
Convergence from both sides
From
OPEN-O
3rd
Legend:
Alarm Correlation App (Holmes)
Workflow Design
VNF Design
Certification & Lab
Modeling (specs & Utilities)
DMaaP
Auth.
Multi VNFM/EMS Driver
GVNFM
Infra-C
New
ESR
Catalog

## Slide 13: From ECOMP: Design & Run Time & Close Loop
Mediation Layer
Design-time
SDC
VNF SDK
Dashboard OA&M
(VID)
A&AI
DCAE
SDN Hub Driver
Service
Orchestrator
GS-O
External Data Movement & APIs
Common Service
Microservice Bus
Multi-VIM
NFV-O NFV Collector
(Monitor)
Run-time
Portal
OPEN-O UI
(GUI/CLI)
Integration
Cloud & WAN
OpenStack
Azure
VMware
RackSpace
......
UI Server
E-Services
BSS/OSS
Big Data
Policy
From
openECOMP
Convergence from both sides
From
OPEN-O
3rd
Legend:
Alarm Correlation App (Holmes)
Certification & Lab
Modeling (specs & Utilities)
DMaaP
Auth.
Multi VNFM/EMS Driver
New
ESR
Catalog
Policy Creation
Analytic Application Creation
Recipie/
Engineering Rules & Policy Distribution
Controllers
SDN Agent
(SDN-O)
VF-C
NFV-O
SDN-C
APP-C
GVNFM
Infra-C
Service Design
VNF Design
Workflow Design

## Slide 14: From OPEN-O: open TOSCA model
Mediation Layer
Design-time
Service Design
Policy Creation
Analytic Application Creation
Recipie/
Engineering Rules & Policy Distribution
SDC
VNF SDK
Dashboard OA&M
(VID)
A&AI
DCAE
SDN Agent
(SDN-O)
SDN Hub Driver
VF-C
NFV-O
SDN-C
APP-C
Service
Orchestrator
GS-O
External Data Movement & APIs
Common Service
Controllers
Microservice Bus
Multi-VIM
NFV-O NFV Collector
(Monitor)
Run-time
Portal
OPEN-O UI
(GUI/CLI)
Integration
Cloud & WAN
OpenStack
Azure
VMware
RackSpace
......
UI Server
E-Services
BSS/OSS
Big Data
Policy
From
openECOMP
Convergence from both sides
From
OPEN-O
3rd
Legend:
Alarm Correlation App (Holmes)
Workflow Design
VNF Design
Certification & Lab
Modeling (specs & Utilities)
DMaaP
Auth.
Multi VNFM/EMS Driver
GVNFM
Infra-C
New
ESR
Catalog

## Slide 15: From OPEN-O: open source process & tools
Mediation Layer
Design-time
Service Design
Policy Creation
Analytic Application Creation
Recipie/
Engineering Rules & Policy Distribution
SDC
VNF SDK
Dashboard OA&M
(VID)
A&AI
DCAE
SDN Agent
(SDN-O)
SDN Hub Driver
VF-C
NFV-O
SDN-C
APP-C
Service
Orchestrator
GS-O
External Data Movement & APIs
Common Service
Controllers
Microservice Bus
Multi-VIM
NFV-O NFV Collector
(Monitor)
Run-time
Portal
OPEN-O UI
(GUI/CLI)
Integration
Cloud & WAN
OpenStack
Azure
VMware
RackSpace
......
UI Server
E-Services
BSS/OSS
Big Data
Policy
From
openECOMP
Convergence from both sides
From
OPEN-O
3rd
Legend:
Alarm Correlation App (Holmes)
Workflow Design
VNF Design
Certification & Lab
Modeling (specs & Utilities)
DMaaP
Auth.
Multi VNFM/EMS Driver
GVNFM
Infra-C
New
ESR
Catalog

## Slide 16: From OPEN-O: Ease of VNF Insertion
Mediation Layer
Design-time
Service Design
Policy Creation
Analytic Application Creation
Recipie/
Engineering Rules & Policy Distribution
SDC
VNF SDK
Dashboard OA&M
(VID)
A&AI
DCAE
SDN Agent
(SDN-O)
SDN Hub Driver
VF-C
NFV-O
SDN-C
APP-C
Service
Orchestrator
GS-O
External Data Movement & APIs
Common Service
Controllers
Microservice Bus
Multi-VIM
NFV-O NFV Collector
(Monitor)
Run-time
Portal
OPEN-O UI
(GUI/CLI)
Integration
Cloud & WAN
OpenStack
Azure
VMware
RackSpace
......
UI Server
E-Services
BSS/OSS
Big Data
Policy
From
openECOMP
Convergence from both sides
From
OPEN-O
3rd
Legend:
Alarm Correlation App (Holmes)
Workflow Design
VNF Design
Certification & Lab
Modeling (specs & Utilities)
DMaaP
Auth.
Multi VNFM/EMS Driver
GVNFM
Infra-C
New
ESR
Catalog

## Slide 17: Looking forward: Multiple Vendors Environment
Mediation Layer
Design-time
Service Design
Policy Creation
Analytic Application Creation
Recipie/
Engineering Rules & Policy Distribution
SDC
VNF SDK
Dashboard OA&M
(VID)
A&AI
DCAE
SDN Agent
(SDN-O)
SDN Hub Driver
VF-C
NFV-O
SDN-C
APP-C
Service
Orchestrator
GS-O
External Data Movement & APIs
Common Service
Controllers
Microservice Bus
Multi-VIM
NFV-O NFV Collector
(Monitor)
Run-time
Portal
OPEN-O UI
(GUI/CLI)
Integration
Cloud & WAN
OpenStack
Azure
VMware
RackSpace
......
UI Server
E-Services
BSS/OSS
Big Data
Policy
From
openECOMP
Convergence from both sides
From
OPEN-O
3rd
Legend:
Alarm Correlation App (Holmes)
Workflow Design
VNF Design
Certification & Lab
Modeling (specs & Utilities)
DMaaP
Auth.
Multi VNFM/EMS Driver
GVNFM
Infra-C
New
ESR
Catalog

## Slide 18: Outline
Requirements from ONAP Use cases
Merger Architecture Proposal Overview
Merger Architecture Highlights
  ONAP Modeling
  ONAP Common Service
  ONAP Service Orchestrator
  ONAP Controllers
    Overview
    VF-C
    SDN-Agent
  Template Driven Closed Loop
  Support for Design, Schedule and Execute Changes (e.g. Software Upgrades)
  VNF SDK
  Resource and Placement Optimization
  Operations Management Framework (OMF)
  Support for Multiple Infrastructure Environments

## Slide 19: ONAP Modeling Overview
Tosca/Yang/Hot template and data modeling for VNF and Service
A common informational model specification for different data modeling
Parser and translator code about NFV data modeling and tools
Policy model specify EMF and SUPA

## Slide 20: Landscape of modeling in ONAP
SO
Network-C
L1-L3
Infra-C
APP-C
L4-L7
VNF-C
NFVO
GVNFM
SVNFM
EMS
VNF in DC
(lb, fw…)
OPENSTACK
SDN
Controller
Runtime
VNF in Core
(EPC, IMS…)
Design
SDC
Policy
Network Device
TOSCA
FCAPS
Service Conf.
TOSCA
TOSCA
YANG
YANG
YANG
YANG
YANG
YANG
YANG
TOSCA
YANG
YANG
Management
Model
Deployment
Model
RESTCONF
Policy
DCAE
TOSCA
A&AI
DG
HEAT
HEAT
HEAT
DG
DG
DG
YANG
HEAT
Policy
BPEL
BPEL
HEAT
CINDER
NEUTRON
SWIFT
GLANCE
BPEL
ODL
EMF
EMF
EMF
NETCONF

## Slide 21: VNF Modelling
HOT
(ECOMP)
TOSCA
(TOSCA NFV)
YANG
(ETSI NFV)
Onboarding
(VNF SDK)
Design
(SDC)
Catalog
LCM
(MSO, APP-C, VNF-C, SDN-C, etc.)
Vendors
Design-time
Run-time
Provider
Different DMs are used for VNF templates. ECOMP uses HEAT, OPEN-O uses TOSCA.
We will be working together on supporting HEAT, TOSCA and YANG VNF modeling.
The core implementation engine for LCM and operation in run time should be data model agnostic.
Parser
(ECOMP)
Parser
(TOSCA)
Parser
(YANG)
Translators
(Utilities)

## Slide 22: Outline
Requirements from ONAP Use cases
Merger Architecture Proposal Overview
Merger Architecture Highlights
  ONAP Modeling
  ONAP Common Service
  ONAP Service Orchestrator
  ONAP Controllers
    Overview
    VF-C
    SDN-Agent
  Template Driven Closed Loop
  Support for Design, Schedule and Execute Changes (e.g. Software Upgrades)
  VNF SDK
  Resource and Placement Optimization
  Operations Management Framework (OMF)
  Support for Multiple Infrastructure Environments

## Slide 23: ONAP Common Service
Functionalities
  Service Registration & Discovery for Micro Services
  Centralized Authentication and Authorization
  Centralized User Management
Benefits
  Mitigate Code Complexity by Avoiding Multiple Point to Point Service Access
  Decouple business logic and UI by Removing Cross Domain Solution

## Slide 24: MSB Solution for ONAP: Service Discovery & Routing
MSB
External Service
gateway
Service Discovery
Internal API Router
Other Modules …
VF-C
Before:
……
How to call service:
After:
"apigateway": "https://apigateway.onap.org:80"
GET https://apigateway.onap.org/api/aai/v8/cloud-infrastructure/cloud-regions/cloud-region/{cloud-owner}/{cloud-region-id}
API gateway routes the request to:
GET https://c1.vm1.aai.simpledemo.openecomp.org:8443/aai/v8 /cloud-infrastructure/cloud-regions/cloud-region/{cloud-owner}/{cloud-region-id}
Using a configuration file, we might have problems on scaling, failover and update
MSB handles the service discovery & routing & LB
MSB as the single entry point

## Slide 25: MSB Solution: Centralized Auth with Plugin(SSO)
MSB
Auth Plugin
API Monitoring
Logging
Other Plugin
User
Admin
ONAP Services
Auth Service
Other Services
Centralized Authentication
User send a service request to MSB
MSB auth plugin check the auth token
2.1 If a valid token exist, MSB forward the request to the destination service provider
2.2 If not, MSB forward the request to the Auth Service, and redirect user request to login page
2.3 Auth service create a token cookie after user login with valid name and password
Centralized Authorization(Assuming user already login)
User send a service request to MSB
MSB auth plugin send the user token and request(Http method + Resource url) to Auth Service
2.1 If user has the permission, MSB forward the request to the destination service provider
2.2 If not, MSB return operation not allowed error to user
Centralized User, Role and Permission Management
Centralized in the Auth Service
Note: Auth Service is not in the scope of MSB
Business requests
Management
requests
Notes: Services typically need to call one another. In a monolithic application, the components invoke one another through language-level method or procedure calls.
In a traditional distributed system deployment, services run at fixed, well known locations (IP address and port)，your code can read the network locations from a configuration file that is occasionally updated.
However, a modern microservice-based application typically runs in a virtualized or containerized environments, Service instances have been dynamically assigned network locations. Moreover, the set of service instances changes dynamically because of autoscaling, failures, and upgrades. So, it’s impossible anymore to use a configuration file to get the locations of your services.

## Slide 26: Outline
Requirements from ONAP Use cases
Merger Architecture Proposal Overview
Merger Architecture Highlights
  ONAP Modeling
  ONAP Common Service
  ONAP Service Orchestrator
  ONAP Controllers
    Overview
    VF-C
    SDN-Agent
  Template Driven Closed Loop
  Support for Design, Schedule and Execute Changes (e.g. Software Upgrades)
  VNF SDK
  Resource and Placement Optimization
  Operations Management Framework (OMF)
  Support for Multiple Infrastructure Environments

## Slide 27: Two Layers of Service Orchestration
DCI SDN Controller
Domain A
OS
vCPE
OS
vLB
OS
vFW
Domain Service Orchestrator
TIC-Edge
TIC-Core
OS
vCPE
OS
vFW
WAN
DC GW
DC GW
Domain B
OS
vCPE
OS
vLB
OS
vFW
Domain Service Orchestrator
OS
vCPE
OS
vFW
Global Service Orchestrator
DC Controller
DC Controller
TIC-Edge
TIC-Core
DC Controller
DC Controller
DC GW
DC GW
WAN
Controller
Case 1: lager scale SPs
Case 2: Federated Orchestration
SO
Notes: In the lager scale SPs, the SPs have a deployment requirement that the E2E Service Orchestrator deployed in the higher location and NFV Orchestrators and VNF Management deployed to the lower location near the managed VNFs to satisfy the high availability and performance.
Some SPs have the cross-country services and need to coordinate other SP’s NFV network resources. They want to use the Service Orchestrator to invoke other SP’s NFV Orchestrator and VNF Management to achieve an E2E network service.

## Slide 28: Workflow for Service Orchestration
Declarative (topology) workflow v.s. imperative workflow
  Topology driven workflow couples topology modeling with workflow
    Issue 1: Not suitable for workflows that cannot be deduced from service topology template
      E.g. for interactions with entities outside service template (A&AI, Catalogue, etc.)
    Issue 2: Not flexible enough for dynamic workflow, e.g. runtime status dependent
      E.g. for location based deployment of VFs among multiple DCs
      E.g. dynamic software upgrade workflow based on runtime HA active-backup status
  Imperative workflow decouples topology modeling from workflow
    Addresses the above two issues
    Allows the core workflow specification & execution implementation be topology template agnostic
    Avoids complex workflow translation when switching between TOSCA/YANG/HEAT template DM
TOSCA provides both built-in topology and imperative workflow in a single template
  Work in progress for TOSCA built-in imperative workflows, addresses Issue 2 but cannot solve Issue 1.
  Joint Proposal to extend TOSCA specification to allow for external BPMN/BPEL workflow to address the above issues and be compliant with existing implementations.

## Slide 29: Alternatives for TOSCA Service Orchestration Workflow
BPMN
Service Orchestrator
TOSCA
Orchestrator
Request
Determine top-level workflow
Load
Invoke
Rainy Day Option:
Invoke Inverse
Success/Fail
Invoke Operation Implementation
Option 1: Topology & BPMN Hybrid Workflow
Option 2: Decoupled 2 layer BPMN Workflow
BPMN
Domain Service Orchestrator
Determine top-level workflow
Invoke
Success/Fail
Request
Service Agnostic WFs
(one for each LCM op)
Service Specific WFs
BPMN
Global Service Orchestrator
Determine top-level workflow
Request
Service Agnostic WFs (one for each LCM op)

## Slide 30: ONAP TOSCA-based Orchestration Work Proposal – Option 1
Description:
Propose expansion of ONAP to include a declarative topologically-driven approach to orchestration, in addition to imperative BPMN/BPEL capabilities
  Enhance ONAP SDC design framework to support integrated or independent use of declarative (TOSCA) and imperative (BPMN/BPEL) models
  Enhance ONAP run-time orchestration to process TOSCA models and workflows
  While TOSCA is native for cloud resources, BPMN/BPEL imperative orchestration is currently more suitable for supporting complex lifecycle management scenarios
Benefits
  Provide a rich design environment supporting declarative and imperative orchestration options
  Single template for orchestrating service/resource instantiation and lifecycle management
  TOSCA is designed for cloud resources and therefore can natively support applications to be instantiated on cloud infrastructure platforms
Use Cases for Applying TOSCA-based Orchestration in ONAP:
VNF and Service instantiation using TOSCA templates on cloud platforms
  TOSCA template created by ONAP SDC design platform and deployed to other components for orchestration
  Common template supporting various cloud based technologies such as VM (e.g., Openstack), Containers (e.g., Docker), Container cluster management (e.g., Kubernetes)
TOSCA-based template model integrates multiple lifecycle management actions and workflows
  Instantiation
  Closed loop actions (restart, stop, self-heal, scale out/scale in, etc.)
  Change management (software upgrades, reconfiguration of VNFs)
Service instantiation in a tiered approach employing both TOSCA and BPMN/BPEL
Note: TOSCA-based orchestration is also being introduced in the ECOMP Controller proposal for ONAP component software management

## Slide 31: TOSCA-based Orchestration: Option 1
SDC
BPMN
AT&T Proprietary (Restricted)
Service Orchestrator
TOSCA
Orchestrator
Request
Determine top-level workflow
Load
Invoke
Rainy Day Option:
Invoke Inverse
Success/Fail
Invoke Operation Implementation
The TOSCA Orchestrator uses the Service Template to determine the proper Operations and sequencing thereof on the various Node Types
Upon receipt of a SO request, initiate appropriate top-level BPMN workflow.
For each BPMN work step that delegates to the TOSCA Orchestrator:
Determine the associated TOSCA Service Template and associated Inputs
load into the TOSCA Orchestrator
Call TOSCA Orchestrator to perform the relevant action
Service Model
Design
Catalog
Service Model
Service Model
Resource Model
Resource Model
Resource Model
Service Model
Runtime
Catalog
Service Model
Service Model
Resource Model
Resource Model
Resource Model
Model Distribution
Metadata Model Driven Orchestration
Execution Time
Preference to keep as simple as possible, to promote Declarative processing approach
Design Time
Tools for Declarative & Imperative Model Design

## Slide 32: ONAP TOSCA-based Orchestration Proposal – Option 2
Implementation Proposal
  Standard TOSCA parser decoupled from workflow execution
  BPMN/BPEL workflow engine for two layer workflows
High level architecture principles
  Be Decoupled and micro-serviced based
  Be practical or available on time
  Leverage what is available and mature and do not reinvent the wheel
Notes: OPEN-O architecture principles
  Be Decoupled and micro-serviced based” is very important, the Selection should not cause us to bind with one special platform/product and no other choice, or bind to a large platform that must be integrated before provide the required service.
  Be practical or available on time, yes, it’s principle for all open source community. All selections should be able catch up with our deliver plan, don’t lets all others wait for that selection to be mature.
  Do not reinvent the wheel, so that it ‘s encourage to reuse or interwork with exist product or solution.

## Slide 33: ONAP TOSCA-based Orchestration Proposal: Option 2
SDC
BPMN
AT&T Proprietary (Restricted)
Domain Service Orchestrator
Request
Determine top-level workflow
Invoke
Success/Fail
The same BPMN workflow engine executes the two layer service workflows.
Upon receipt of a SO request, initiate appropriate top-level BPMN workflow.
For each service agnostic work step that delegates to the next level of workflow:
Determine the associated service workflow and associated Inputs
perform the relevant action
Service Model
Design
Catalog
Service Model
Service Model
Resource Model
Resource Model
Resource Model
Service Model
Runtime
Catalog
Service Model
Service Model
Resource Model
Resource Model
Resource Model
Model Distribution
Metadata Model Driven Orchestration
Execution Time
Design Time
Tools for Imperative Model Design
Service Agnostic WFs
Service Specific WFs

## Slide 34: Outline
Requirements from ONAP Use cases
Merger Architecture Proposal Overview
Merger Architecture Highlights
  ONAP Modeling
  ONAP Common Service
  ONAP Service Orchestrator
  ONAP Controllers
    Overview
    VF-C
    SDN-Agent
  Template Driven Closed Loop
  Support for Design, Schedule and Execute Changes (e.g. Software Upgrades)
  VNF SDK
  Resource and Placement Optimization
  Operations Management Framework (OMF)
  Support for Multiple Infrastructure Environments

## Slide 35: ONAP Controller Framework
SDN-C
APP-C
API Handlers
Service Logic Interpreter
SDN-C Database
Service Logic/Eng Rules
Assigned Inventory
Config
Tree
Operational Tree
Adaptors
Adaptors
Adaptors
Compiler
Configuration Repository
MD-SAL Context DB
Service Topology & VF State
Operational & Config Tree
(Svc Model)
Policy Cache & Event Matching
Service Logic Interpreter
Adaptors
Adaptors
Adaptors
Service Logic Execution
Adaptors
Adaptors
Adaptors
…
SDN Agent
API Handlers
Compiler
Policy Cache &
Event Matching
Service Logic Execution
Adaptors
Adaptors
Adaptors
…
VF-C
API Handlers
Compiler
Policy Cache &
Event Matching
3rd Party Controller
VNFM / EMS
3rd Party Controller
3rd Party Controller
VNFM / EMS
VNFM / EMS
Service Orchestrator
Summary:
  ONAP Controller Family include SDN-C, APP-C, SDN Agent & VF-C
  SND Agent for interfacing with third party controller and VF-C for interface with Vendor VNFM /EMC
  Service Orchestrator will call the right controller, depending on the VNF being managed
  Goal is create as much commonality between controller as possible, to the rest of ONAP all controllers look and behave the same way

## Slide 36: Outline
Requirements from ONAP Use cases
Merger Architecture Proposal Overview
Merger Architecture Highlights
  ONAP Modeling
  ONAP Common Service
  ONAP Service Orchestrator
  ONAP Controllers
    Overview
    VF-C
    SDN-Agent
  Template Driven Closed Loop
  Support for Design, Schedule and Execute Changes (e.g. Software Upgrades)
  VNF SDK
  Resource and Placement Optimization
  Operations Management Framework (OMF)
  Support for Multiple Infrastructure Environments

## Slide 37: VF-C Introduction
Using ETSI NFV MANO architecture and information model as a reference, and targeted at implementing the NFV-O/GVNFM Component that provides orchestration for Network Services composed of Virtualized Network Functions and general VNF management.
NFV domain network service automation delivery via VF-C is at the heart of realizing service agility, which significantly reduces time to market for new service offerings and reduces CAPEX/OPEX.
Multi VNF Manager, EMS and VIM integration via drivers enables ONAP to manage more different vendor VNFs
Multi NS/VNF templates via different parsers enable more SDO data models(TOSCA/Yang/Heat, etc) to be instantiated.
Notes: Service Agility has been the major promise of SDN/NFV to service providers in transforming their legacy infrastructure into the virtualization paradigm.
Automation of service delivery via NFV orchestration is at the heart of realizing service agility, which significantly reduces time to market for new service offerings and reduces CAPEX/OPEX.
This project is targeted at implementing the NFV-O Component that provides orchestration for Network Services composed of Virtualized Network Functions, as an integral part of ONAP.
This project is also targeted at implementing plugins/drivers to enable support for multiple VIM, VNFM or EMS from different vendors.

## Slide 38: How VF-C Fit into ONAP Architecture
Virtual Function Controller (VF-C)
Portal
NS&VNF LCM
Create/Delete/… Virtual Resources
A&AI
Inventory
VNF
VNF
SO
SDC
Policy
NS/VNF Package
vCE
VNF
Cloud
VNF
Distribution Service
VNFM
EMS
VIM
3rd SFC Controllers
3rd VNFMs
Inventory Data CRUD
3rd VIMs
Adaptor
Adaptor
Adaptor
Create/Delete/… ViNF
Config/…
ViNF
3rd SFC Controllers
Create/delete/…
SFC
ONAP
Portal/SDC/MSO/Policy add adaptor for VF-C RESTAPI
VF-C add adaptor for A&AI\Common services,etc
DCAE collects data from EMS via new adaptor
Adaptor
Common Services
DCAE
3rd EMSs
FM/PM…
Adaptor
Extension

## Slide 39: VF-C Solution : VFC Components& Main Features
API Handler
Drivers
3rd EMS Driver
3rd VNFM Drivers
3rd EMS Driver
3rd EMS Drivers
3rd EMS Driver
3rd EMS Driver
VIM Drivers
NFV Lifecycle Management
3rd EMS Driver
3rd EMS Driver
3rd SFC Drivers
Workflow Engine
NFV
Information Model
Wo
W
Workflow Templates
    Support BPMN/BPEL workflow
    Support NFV information Model and multi data models
    Support ETSI architecture and IFA interfaces
    Support VNF EPA features
    Integrated with 3rd VNFMs and VNF, such as Ericsson, JUJU, Huawei, and ZTE, etc
    Integrated with multiple cloud systems, such as redhat, vmware, windriver, and unbantu, etc

## Slide 40: Outline
Requirements from ONAP Use cases
Merger Architecture Proposal Overview
Merger Architecture Highlights
  ONAP Modeling
  ONAP Common Service
  ONAP Service Orchestrator
  ONAP Controllers
    Overview
    VF-C
    SDN-Agent
  Template Driven Closed Loop
  Support for Design, Schedule and Execute Changes (e.g. Software Upgrades)
  VNF SDK
  Resource and Placement Optimization
  Operations Management Framework (OMF)
  Support for Multiple Infrastructure Environments

## Slide 41: Outline
Requirements from ONAP Use cases
Merger Architecture Proposal Overview
Merger Architecture Highlights
  ONAP Modeling
  ONAP Common Service
  ONAP Service Orchestrator
  ONAP Controllers
  Template Driven Closed Loop
  Support for Design, Schedule and Execute Changes (e.g. Software Upgrades)
  VNF SDK
  Resource and Placement Optimization
  Operations Management Framework (OMF)
  Support for Multiple Infrastructure Environments

## Slide 42: Closed-Loop Repeating Design Pattern
Storage
Compute
Network
Applications
Storage
Compute
Applications
Service
Elements
Compute
NFV Elements
Policy
Orchestration
Controller
Cloud Elements
Loop
DCAE
Policy
Orchestration
Controller
Loop
DCAE
Policy
Orchestration
Controller
Loop
DCAE
Service
Network Functions
Cloud

## Slide 43: Control Loop Design and Execution Flow
Control Loop Runtime Execution Example
VF
Source
VES
DCAE Collector
TCA
CDAP
DCAE Analytic
Docker
Policy Engine
Signature Detected
DROOLS
Policy
App-C
DMaaP
Action
Execution
Initiate
Action
NETCONF
Control Loop Design Time
Control Loop
Management Cockpit
Query services, VNFs
Get performance counter file
Submit closed loop for distribution
Policy
Engine
Create and
Activate policies: TCA
and
Operational,
Stop/Start,
Reconfigure
SDC
Onboard VNF,
Alarm file and
create service
Create template,
Configure CL,
Deploy CL,
Stop/Restart,
Reconfigure
DCAE Inventory
DCAE
DCAE Dispatcher
Cloudify
(includes plugins)
CDAP Broker
TCA
CDAP
Deploy
control loop
Service Change Handler
Databus Controller
Test, Certify,
Distribute
Closed Loop
Check
distribution status
Docker
VES Collector
Distribute Control loop

## Slide 44: Outline
Requirements from ONAP Use cases
Merger Architecture Proposal Overview
Merger Architecture Highlights
  ONAP Modeling
  ONAP Common Service
  ONAP Service Orchestrator
  ONAP Controllers
  Template Driven Closed Loop
  Support for Design, Schedule and Execute Changes (e.g. Software Upgrades)
  VNF SDK
  Resource and Placement Optimization
  Operations Management Framework (OMF)
  Support for Multiple Infrastructure Environments

## Slide 45: VNF Change Management Process
Design:
Building blocks for individual tasks
Design workflow as a composition of building blocks
Scheduling:
Schedule optimization for avoiding conflicts
Conflict rules as policies
Execution:
Automated workflow orchestration and tracking
Ability to intercept execution – pause/resume
Policy enabled go/no-go
Improved manageability: Systematic design of workflow, scheduling and execution
Minimize service disruption: conflict avoidance for schedule and automated roll-out/fall-backs

## Slide 46: CM Process Design
  CM Designer
Modular composition to stitch different building blocks into a workflow (using a visual designer) e.g., In-place software upgrade, Build and Replace.
SDC (catalog)
A&AI
Controllers
(APP-C, SDN-C)
DCAE
  CM Building Blocks in Catalog
DCAE micro-services, A&AI APIs, Controller capabilities (e.g., health check APIs), scripts/workflows.
Onboard component
capabilities
SDC (CM catalog)
SDC (CM Designer)

## Slide 47: Change Management Scheduling & Conflict Avoidance
  CM Schedule Optimizer -> SNIRO
  Create a schedule/plan for rolling out a change such that we minimize service disruption during the change within the specific completion time
  Dependency modeling
    Conflict scoping
    Service Impact scoping
    Execution ordering
1 – Send workflow, VNF list and time range to SNIRO
2 – Request constraints for scheduling
3 – Request data for schedule optimization
4 – Identify CM schedule
5 – Provide the schedule for approval
6 – Once approved, send the schedule to Change tracking/notification OSS.
7 – Push the approved change schedule for execution
CM Orchestration
CM schedule optimizer (SNIRO)
ONAP Portal
CM Portal
1
A&AI
DCAE
3
7
Tracking/ Notification OSS
6
3
4
5
Policy
2
3

## Slide 48: Change Execution
  Orchestration Execution:
  Execute the orchestration building blocks and use RESTAPIs to interface controller for software upgrade, or A&AI for updates to the CM flag
  ONAP Portal:
  Track status of CM workflow execution – success/failure status of each building block
  Intercept CM workflow execution – pause/resume functions, and ability to inject new steps in the workflow
  Pre / Post Analytics:
  Performance analytics – pre/post performance comparisons, go/no-go decisions for network-wide deployment
1 – Start execution based on schedule
2 – Conflict check
2b – Check roll-out status
3 – (Pre) health check
4 – Update CM flag
5 – VNF upgrade
6 – (Post) health check
7 – Pre/post impact analysis
7b – Fallback (possibly)
8 – Update CM flag
** – Status tracking and pause/resume execution at any/all times
Orchestration
A&AI
Controllers
(APP-C, SDN-C, SDN-O, MCAP)
DCAE
5
7
**
ONAP Portal
CM Portal
1
7b
6
3
4
8
Policy
2
2b

## Slide 49: Outline
Requirements from ONAP Use cases
Merger Architecture Proposal Overview
Merger Architecture Highlights
  ONAP Modeling
  ONAP Common Service
  ONAP Service Orchestrator
  ONAP Controllers
  Template Driven Closed Loop
  Support for Design, Schedule and Execute Changes (e.g. Software Upgrades)
  VNF SDK
  Resource and Placement Optimization
  Operations Management Framework (OMF)
  Support for Multiple Infrastructure Environments

## Slide 50: VNF Onboarding SDK
Description:
  Propose to build an SDK and automation/devOps tools for VNF onboarding.
    This functionality uses VNF guidelines & information model as needed.
    This project implements methods and processes for VNF vendors to onboard ONAP compliant VNF packages to Service Providers or market place, including automated ingestion to Design Platform (SDC).
    This project focuses on the SDK tools, not ONAP business models (e.g., market place).
  Benefits:
    Provide a standard packaging and submission process for VNF vendors to multiple ONAP service providers.
    Enforce VNF packages to meet ONAP standards and requirements for deployment and lifecycle management of the VNF products.
    Reduce the costs of onboarding and to provide speedy time-to-market of the VNFs.
Use Cases:
  Vendor uses SDK to validate VNF package.
  Service Provider uses SDK to automate ingestion of a VNF package to SDC Design Platform.

## Slide 51: VNF Onboarding SDK
SP’s SDC
SP’s SDC
SDK
Create & Validate
SDK Validate & Onboard
Supplier A
SDK Validate & Onboard
Supplier B
SDK
Create & Validate
Market Place
VNF Catalog
Certified VNF
Package
Supplier A
ONAP Compliant
SP additional Validation & Onboarding
ONAP Compliant
VNF
Package
1. Service Provider Option
3. Marketplace Option
Certified VNF
Package
Certified VNF
Package
SP additional Validation & Onboarding
Supplier B
VNF
Package
VNF
Package
VNF
Package
2. Supplier-SP Option
SP’s SDC
SDK
Create & Validate
SDK Validate & Onboard
Supplier A
Certified VNF
Package
ONAP Compliant
SP additional Validation & Onboarding
VNF
Package
Supplier B
VNF
Package
SDK
Create & Validate
Certified VNF
Package
Optionally to include SP specific configuration changes

## Slide 52: Outline
Requirements from ONAP Use cases
Merger Architecture Proposal Overview
Merger Architecture Highlights
  ONAP Modeling
  ONAP Common Service
  ONAP Service Orchestrator
  ONAP Controllers
  Template Driven Closed Loop
  Support for Design, Schedule and Execute Changes (e.g. Software Upgrades)
  VNF SDK
  Resource and Placement Optimization
  Operations Management Framework (OMF)
  Support for Multiple Infrastructure Environments

## Slide 53: ONAP Optimization Framework (ONAP-OF)
Background:
    Optimization was an early concept in ECOMP (to many objects for manual mechanisms)
    Spans Service, Network, Infrastructure, and Resources
    ECOMP has four (4) optimizers today:
      Placement
        Within a cloud instance
        Integrated with OpenStack
      Homing
        Spans cloud instances
        Policy driven
        Provides ability for business, service, and network rules to be used in selecting locations for service resources
      License
        Selects Software Entitlements and License Keys for software being deployed or reconfigured
        Allows complex criteria, conformant to contractual constrictions to be used
        Allows for business rules to drive cost reductions in entitlements used
      CM Schedule
        Uses Rules to avoid conflicts between related elements during scheduled software change/upgrade activities
        Evaluates Vertical Relationships (implementation stack)
        Evaluates Horizontal Relationships (service path)
The ONAP Optimization Framework (ONAP-OF) is being proposed as a new platform component that to introduce the Homing, License and Change Management Schedule optimizers in an manner that allows other implementers to also extend or replace the optimizations supported with their specific optimizers.

## Slide 54: ONAP Optimization Framework (ONAP-OF) Proposal
ONAP-OF SCOPE
Develop an extensible framework to deploy optimization applications for ONAP
    Provide standard interface for optimization requests from other ONAP entities.
    Interact with ONAP-C for micro service management
    Provide Management framework that will allow:
      New Optimizers Applications to be deployed in a distributed manner
      Provide ability to add Optimization Data Providers
      Provide ability to add new data sets that can be provided by a Data Provider
Provide three (3) sample Optimizers
    Homing allows selection of cloud instances to be used for service components
    License allows complex criteria to be used in selecting software entitlements and license keys needed to enable deployed software
    CM Schedule allows policy to dictate conflicts to avoid when attempting to establish a schedule for a large number of SW instances requiring modification.
ONAP-OF Reference Architecture

## Slide 55: Outline
Requirements from ONAP Use cases
Merger Architecture Proposal Overview
Merger Architecture Highlights
  ONAP Modeling
  ONAP Common Service
  ONAP Service Orchestrator
  ONAP Controllers
  Template Driven Closed Loop
  Support for Design, Schedule and Execute Changes (e.g. Software Upgrades)
  VNF SDK
  Resource and Placement Optimization
  Operations Management Framework (OMF)
  Support for Multiple Infrastructure Environments

## Slide 56: ONAP : Operations Management Framework (OMF)
  OMF Portal : Provides GUI for operations team to perform tasks such as:
    Request for Network Configuration Change
    Execute workflow for network change
    Administrative tasks such as Role based access to OMF
    Execute test case
  OMF Middleware :
    Business Logic Layer : implement O&M functions as uS and reusable components e.g. New Service Rollout Mgmt
    Integration Layer : Build cartridges/adaptors to interface with external systems.
  OMF Configuration Engine
    Manage, Perform and Orchestrate Service level Configuration changes
  OMF Test Engine
    Perform Service Regression, Validation tests, Device Health check Tests.

## Slide 57: Outline
Requirements from ONAP Use cases
Merger Architecture Proposal Overview
Merger Architecture Highlights
  ONAP Modeling
  ONAP Common Service
  ONAP Service Orchestrator
  ONAP Controllers
  Template Driven Closed Loop
  Support for Design, Schedule and Execute Changes (e.g. Software Upgrades)
  VNF SDK
  Resource and Placement Optimization
  Operations Management Framework (OMF)
  Support for Multiple Infrastructure Environments

## Slide 58: Multiple Infrastructure Support Abstraction Layer
Enhancement Summary:
  Expand ONAP SDC to Capture Artifacts to Support Multiple Infrastructure Environment
  Create an Infrastructure Abstraction Layer with Adaptors for Various Infrastructures
  Service Orchestrator and other ONAP Applications will Interface with the Abstraction Layer with right template
  Infrastructure Abstraction Layer will Interact with Different Infrastructures and pass right templates
  This is a very high level view, additional design details to be worked with the TSC controller sub-group.
Under Development
Design Environment
Execution Environment

## Slide 59: Multiple Infrastructure Support
Logic Engine to
validate/dispatch/verify
physical Adaptor
Multi-vim Adaptor
Infrastructure -C
API Handler
Physical Host
Container
VMware
OpenStack
Registry Manager
Service Orchestrator
VF-C
APP-C
A&AI
SDC
DCAE
Catalog
template
Design time
Run time
collector
  Expand ONAP SDC to Capture Artifacts to Support Multiple Infrastructure Environment
  Create an Infrastructure Abstraction Layer with Adaptors for Various Infrastructures
  Service Orchestrator and other ONAP Applications will Interface with the Abstraction Layer for infrastructure functions
  Infrastructure Abstraction Layer will Interact with Different Infrastructures and pass right templates
  Expand A&AI to contain registries of VIM information
    capabilities
    version
    meta data
  Infrastructure-C to provide one unified entry to multiple infrastructure environments:
      Called by both APP-C and VF-C
            Authentication Federation
            Standard API on infrastructure LCM, health check/recover
            expose monitoring/alerts/events for DCAE or any consumer

## Slide 60: Close Look at Infrastructure-C
Logic Engine to
validate/dispatch/verify
physical Adaptor
Multi-vim Adaptor
Infrastructure -C
API Handler
Physical Host
Container
VMware
OpenStack
Registry Manager
API Handler
    Accept REST request and encapsulate returns
    Taking care of parallelism
Registry Manager:
    Support registry/un-registry of NFVI
    Publish/Update infrastructure capability/version/meta to A&AI service
Logic Engine
    Call Registry Manager and execution validation logic
    Dispatch API calls to different Adaptors/Plugins
    Verify results from Adaptors/Plugins
Multi-vim Adaptor:
    Handle different VNFI including OpenStack(different versions), VMware and so on.
    Expose monitoring metrics/alerts/events for the consumption of DCAE
Physical Adaptor:
    Handle physical host related functions, like fencing for HA recover -- a key step for service resilience
Logic Engine to
validate/dispatch/verify

## Slide 61: BAKCUP SLIDES

## Slide 62: Proposed ONAP Merged Architecture
Storage
Compute
VNFs / Applications
Networking
ONAP Portal
Design Functions
Operational Functions
E – Services BSS / OSS Big Data
External Data Movement & APIs
Data Collection & Analytics
Common Services, Data Movement, Access Control & APIs
Controllers
Service Orchestrator
Active & Available Inventory
Dashboard
OA&M Operation Administration & Maintenance
ONAP Controller
Recipe/Engineering Rules & Policy Distribution
Service Design & Creation
Analytic Application Design
Policy Creation
© 2017 AT&T Intellectual Property. All rights reserved. AT&T, Globe logo, Mobilizing Your World and DIRECTV are registered trademarks and service marks of AT&T Intellectual Property and/or AT&T affiliated companies. All other marks are the property of their respective owners.
Infra.
Cont
network
Cont
App.
Cont
3rd Party Controller
VNFM / EMS
VF
Cont
SDN
Agent

## Slide 63: Proposed ONAP Merged Architecture
Storage
Compute
VNFs / Applications
Networking
ONAP Portal
Design Functions
Operational Functions
E – Services BSS / OSS Big Data
External Data Movement & APIs
Data Collection & Analytics
Common Services, Data Movement, Access Control & APIs
Controllers
Service Orchestrator
Active & Available Inventory
Dashboard
OA&M Operation Administration & Maintenance
ONAP Controller
Recipe/Engineering Rules & Policy Distribution
Service Design & Creation
Analytic Application Design
Policy Creation
© 2017 AT&T Intellectual Property. All rights reserved. AT&T, Globe logo, Mobilizing Your World and DIRECTV are registered trademarks and service marks of AT&T Intellectual Property and/or AT&T affiliated companies. All other marks are the property of their respective owners.
Infra.
Cont
network
Cont
App.
Cont
3rd Party Controller
VNFM / EMS
VF
Cont
SDN
Agent
VNF SDK
Service Orchestrator (SO)
Orchestrates and manages the delivery, modification or removal of networks & services
Provides cross domain orchestration and coordination
Integrate TOSCA end-to-end orchestration
Controllers
Network: Configuration Management of VNFs, infrastructure networking & WANs
Service/App: configures & manages of Service VFs
VF-C: works with DCAE, policy and orchestrator to provide Life cycle and FCAPS management for complicated VNFs, and provides adaptors to support vendor EMS / VNF-Manager
SDN Agent: adaptor for 3rp party controllers.
Infrastructure: Configuration Management of infrastructure (compute, storage, etc.)
Data Collection, Analytics & Events (DCAE)
Collects Telemetry Data from VNFs and other sources
    Analytic Applications Detect Anomalous conditions
    Publishes Actionable conditions
Active & Available Inventory (A&AI)
Real-time topology map with context views of virtual networks, services and applications
Uses the network resources as the database of record due to their dynamic nature
Design Platform
Service Design: environment to define service and resource, constraints, instantiation & modification recipes.
Policy Creation: Associate anomalous and actionable conditions with automated remedy actions
Provides SDK to onboard and certify Vendor VNFs